## Slide 1
Device Template File (DTF) Authoring
Ryan Ackerman, Software Developer

## Slide 2: Overview
What’s a DTF file all about?
How do I use conversion functions?
How do I use reference methods?
How do I know my edits are valid?

## Slide 3: Device Template
What is a template
Design considerations
Similarities between EIEs
Common Attributes
Matching device data

## Slide 4: What is a template?
XML Document
Represents
  Device Data Configuration
  Logical/Normalized Representation of Data
Identifies the type of device in CygNet
Read/Write Access
Notes: Device Data Configuration:
Blocks
Logical Representation
Deids

## Slide 5: Design Considerations
Do I duplicate data?
Is there an advantage to using small data groups?
Are there considerations when executing from a UIS command?
Can I mix and match data from different data groups?

## Slide 6: Similarities between EIEs
General properties
  Device type
  EIE type
Data groups
Data elements
<deviceDefinition deviceType="WESC - SLC" eieType="AllenBradleyCIP" >
<dataGroups …
<float1 type="r4"/>
Notes: Data Groups
Property inheritance (child parent)

## Slide 7: Common Attributes
type=“”
  Device
  CygNet/DDS
byteOrder=“”
cvtF=“”
readOnly=“”
ref=“” isRef=“”

## Slide 8: Matching Device Data
What is this value? 00 00 80 3F
CrcGenerator, Comm data (advanced details)
Data Type / Byte Order | Value
r4 (IEEE 754) / Little Endian | 1
ui4 / Big Endian | 32831
ui2 / Big Endian | 0
ui4 / Big Endian / Word Swap | 16256

## Slide 9: CRC Generator

## Slide 10: Conversion Functions (cvtF)
What purpose do they serve?
Example

## Slide 11: What purpose do they serve?
Additional normalization
Writable
Brevity
Raw source not retained
Notes: Why?
More complex typing

## Slide 12: Available Conversion Functions

## Slide 13: Example
More complex conversion required
Brevity
<BaseStkLen desc="Base Stroke Length"
type="r4"
cvtF="Scale"
sourceType="i2"
scaleFactor="0.1"/>
<CRtmCr desc="Runtime current cycle" cvtF="3ByteTime" type="ui4" units="sec"/>
Source Data | Result
01 09 07 | 4147 (seconds)
Notes: Brevity, as compared to reference methods

## Slide 14: Reference Methods
Basic method
Advanced method

## Slide 15: Reference Methods (Basic)
One to one relationship
Calculated value
Time of calculation
  Display
  Point processing
Read/Write

## Slide 16: Reference Methods (Advanced)
One to many relationship
Values are read only
Extremely flexible
Wide range of features and functions

## Slide 17: Template validation
DTF Manager
Loading templates
Displaying an editor
Loading device driver

## Slide 18: Build Modbus Template (Demo)
Analyze device specification
DtfMgr
Define data groups
  Analog input
  Meter configuration (ordinal)
  Status
  Gas history
  RTU configuration
  Composite data group
Poll the device

## Slide 19
For more information visit:
www.cygnetblog.com

## Slide 20: Event Survey and Prizes
Online survey
  QR code or go to http://ep-weatherford.com/events/2015_WESC/WESC_Survey.html
  2 laptops in registration area
Hardcopies
  Registration desk
  Please stop by the registration desk to get your ticket for the drawing once you have completed the survey
Survey prizes will be drawn at the end of Wednesday in the Session Close!
You must be present to win
Notes: Speaker to remind the audience their feedback is important and to complete and submit the surveys. Two options: either online, QR codes available on signage and at the registration desk. Or pick up a hard copy and complete, turn in to WFT staff at registration desk and pickup a ticket for the drawing. Prize drawn at EOD Wednesday during closing session, must be present to win.